## Slide 1
Activity 4- Designing the front wing.

## Slide 2
You are going to create the front wings on your car.
There will be different shaped wings throughout this guide.

## Slide 3
Origin- Click the arrow next to origin.
Right click YZ and select ‘Create Sketch’
TIP
Ensure the plane is in the middle of the car.

## Slide 4
Ensure you can view the side the car. Use the cube to rotate.
Click ‘CREATE’
Select ‘Ellipse’

## Slide 5
Select the place you would like the middle of the wing.
Drag the cord length of the wing.
Select the thickness of the ellipse- 3mm- 15mm

## Slide 6
You can leave the shape as it is.
However, you can shape the ellipse to be more aerodynamic.

## Slide 7
You can leave the shape as it is.
However, you can shape the ellipse to be more aerodynamic.
Select ‘LINE’- Draw the line across the ellipse.

## Slide 8
Press ‘T’ on your keyboard for the trim tool.
Select the top of the ellipse and double click.
Select ‘Finish Sketch’

## Slide 10
Select the shape you have created.
In the EXTRUDE menu;
Direction- Symmetric
Operation- Join

## Slide 11
Drag the arrows outwards for the wing span.
Minimum- 60mm
Maximum- 80mm
TIP
Symmetric shows only half the measurement e.g 60mm has appeared as 30mm.

## Slide 12
Congratulations, you have created a front wing for your car.
The next few slides show different shaped wings.

## Slide 13
Here is another way of creating the front wings.

## Slide 14
Using the line tool, create a triangle.

## Slide 16
Direction- Symmetric
Operation- Join

## Slide 17
Drag the triangle out
Minimum- 60mm
Maximum- 80mm

## Slide 20
Using the ellipse tool, create an ellipse shape.

## Slide 22
Direction- Symmetric
Operation- Join
Drag the shape out;
Minimum- 60mm
Maximum- 80mm

## Slide 24
Select ‘CREATE SKETCH’
Click the end of the ellipse shape.

## Slide 25
Select ‘CREATE’
Select ‘Rectangle’
Select ‘Centre Rectangle’

## Slide 26
Select the middle of the ellipse.
Create a rectangle

## Slide 28
Select EXTRUDE.
Select the rectangle made.
Operation- Join

## Slide 29
Drag the rectangle outwards.
Remember, the maximum length of the wing- 80mm

## Slide 31
Select CREATE
Select Mirror.

## Slide 32
Select the rectangle you have created on the end of the ellipse.

## Slide 33
Select Mirror Plane in the MIRROR menu
Select the middle plane
Click OK